AMERICAN CAR CRAFT

18701 Old Shady Hill Rd. Spring Hill, Fl. 34610

Phone: 727 857-1151               Fax: 727 856-0273

www.americancarcraft.com

05-06 MUSTANG FUSE BOX COVER

PART#MGFB212 patent pending

INSTALLATION INSTRUCTIONS

PARTS INCLUDED:

1-Stainless Fuse Box Cover

Your new cover comes to you with a protective liner. Do not remove liner until installation is complete.

- Your new fuse box cover is designed to fit between the BCM module up and over the factory fuse box lid and down under the fender ridge. It will be necessary to remove the heavy black wire harness that is attached to the fender and allow this harness to fall below the fender ridge. If your application is for the GT Model you will need to release some wire from this harness in order to allow the pin switch cable to be manipulated around the edge of the new cover.

- In order to except this custom cover it will be necessary to remove the front latch from the factory fuse box cover. This can be done by simply slicing the extruded latch with a utility knife or if you have a grinder it may be easier for you to simply grind the latch smooth. PLEASE NOTE: This step does not compromise the seal and allows the custom cover to be placed over the fuse box offering its own seal and a nice looking front face!

- Once these steps have been done simply place the new fuse box cover into position. Remove the protective liner.

If any questions occur during installation, please contact American Car Craft at 727 857-1151.

Thank you and enjoy your new purchase.

Note: Care must be taken when cleaning your cover. It is a good idea to lightly dust your cover with a clean soft cloth first in order to prevent any particles from scratching it. Then wipe (using a new clean soft cloth) with a good quality streak free glass cleaner.